## Slide 1
Brian Hartvigsen
Manager, Site Reliability Engineering
Real World Impacts of EDNS Client Subnet

## Slide 2
Me
BOI
ISP
SEA
youtube.com
Google
SJC
youtube.com
Google SEA
Google SEA
I see you’re in SEA, we have a DC there…
youtube.com
Google
SEA
Google
SJC

## Slide 3
Me
BOI
ISP
SEA
youtube.com
Google
SJC
youtube.com
Google SJC
Google SJC
I see you’re in DFW, we have a DC in SJC…
youtube.com
Google
SEA
Google
SJC
OpenDNS
DFW

## Slide 4: A Short History
Google/OpenDNS both using option code 0x50FA
2010
2011
…
2015
Renamed EDNS Client Subnet
Draft for EDNS Client IP sent to DNSOP
Announcement of Global Internet Speedup Initiative
Many CDNs & DNS server software add support
Option code 0x08 assigned
Akamai announces support when using OpenDNS or Google
Notes: Global Internet Speedup Initiative announced
  Google, OpenDNS
  Bit Gravity, CDNetworks, Cloudflare, Comodo, Edgecast
PowerDNS (), gdnsd (1.5.3 / 2011-06-03), Knot DNS (1.5.0 / 2014-06-06)
Unbound (contrib patch)
BIND (unofficial patches)
dnspython (dnspython-clientsubnetoption / 2012-09-19)
2014-06-03 OpenDNS & Akamai are talking EDNS client subnet

## Slide 5
Me
BOI
ISP
SEA
youtube.com
Google
SJC
youtube.com
(for BOI)
Google SEA
Google SEA
I see you’re asking for BOI, SEA is good!
Google
SEA
Google
SJC
OpenDNS
DFW
youtube.com

## Slide 6: A Couple Notes on OpenDNS’ implementation
Whitelist Only
Not accepted from client side
Fixed scope, manageable via configuration

## Slide 7: The Setup
Mirror production traffic to 2 resolvers
Identical traffic
~2 weeks of data
Enable ECS on only 1
Monitor

## Slide 8: Start from the user’s perspective
Biggest measure is RTT
~5000 qps
~85% <25ms
~95% <300ms

## Slide 9
Still ~95% <300ms
But only ~80% <25ms
More jitter in RTT

## Slide 10: Cache Hits vs Cache Misses
Cache Miss is no data or record with non-matching ECS info
Every failed lookup = 2 + n number of misses
  n = number of possible ECS enabled records that won’t match (max 16,777,215)
Store ECS ability as a special record in the cache
Every successful lookup == 2 cache hits (special record + actual record)

## Slide 12: Cache Churn
Fixed cache size per resolver
Allocate all available memory
  Bi-directional linked list
Measure cache “cycle”
  How often we run out of room in the cache to store something

## Slide 14: Moving upstream

## Slide 15: Bumps in the Road
Malformed responses
Common one was getting back additional 0 bits in address
  Remember to chop it to NETMASK

## Slide 16: Bumps in the Road
Different A records for nameservers w/ ECS
  example.com NS ns1.example.com
  ns1.example.com A 192.0.2.53 (for 1.2.3.0/24)
  ns1.example.com A 192.0.2.153 (for 1.2.4.0/24)
  ns1.example.com A 192.0.2.253 (no ECS)
  Which records should you use when resolving www.example.com for 1.2.3.0/24?
Discussion and clarification around this is welcome