## Slide 1: Anycast on a shoe string
Nat Morris
10th May 2014 @ DNS-OARC

## Slide 2: About me
Consultant, Esgob Ltd
Engineer, Cumulus
Board member, UKNOF
Based in West Wales
Aspiring lighthouse keeper

## Slide 3: Summary
Fancied deploying a DNS Anycast service
Motivated by:
  Bill Woodcock
    SANOG8: “Best Practices in DNS Anycast Service-Provision”
  Dave Knight
    RIPE64: “Dense Anycast Deployment of DNS Authority Servers”
Gain more experience automating distributed environments.

## Slide 4: Thoughts
Can I do it without spending too much?
Does Claire need to find out?
  Must be sub $1000/yr running cost
What to offer?
  Initially only secondary DNS
  IPv4 + IPv6 (yes Martin!)
  Free service - no SLA

## Slide 5: Requirements
Separation from existing management network - AS30746
Had spare PI /24 + /48
Applied for new ASN - got AS60564
Need highly automated framework
Wanted to play with new tools
Open source everything
  https://github.com/esgob

## Slide 6: DNS zone transfers
AS30746
axfr.esgob.com
Anycast nodes
Zone transfer
Master servers operated by others
ns0.esgob.co.uk
(only my zones)
Zone transfer
AS60564
Supports notifies from masters
Zone transfer

## Slide 7: Store everything in JSON
Data stored in RethinkDB
  Distributed JSON document database
  Free form, easy to add attributes

## Slide 8: Application design
REST API - Python + Flask framework
Beanstalk - Message queue
  Add/change/removal of zones via API triggers job to be added to queues for each node
  Daemons on AXFR + Anycast nodes monitor for jobs
  New zones live on all nodes with 5 seconds
RethinkDB
REST
API
Python + Flask
Website
Python + Flask
Scripts
BeanstalkD
job
job
Config files
Jinja2 templates

## Slide 9: Network
Each anycast node:
  Static default route to the provider
  Announce /24 + /48 via BGP
All management traffic inside OpenVPN
  Additional RFC1918 loopback per node
  No need for TSIG from AXFR to anycast nodes
  Protects beanstalk traffic, collectd, zone transfers
AS30746
axfr.esgob.com

## Slide 10: Where to host the anycast nodes?
Can’t cost too much each month
  Ruled out renting co-lo / dedicated servers
Virtual machines
  Swap with friends?
Low cost hardware

## Slide 11: Mythic Beasts
UK clueful hosting company
£7/month = £84/yr = $141/yr
  512mb RAM, 1 CPU, 10gb HDD, 75gb BW
Bought a VM, opened a support ticket
  BGP not listed on the website.
  Me: “I have a /24 + /48 of PI, can you set me up a BGP session?”
  Them: “Peer with these IPs, sessions are ready!”
Too easy!

## Slide 12: Quest to find more friendly VM hosts
LowEndBox.com
  Blog / adverts for VM providers, all < $10 month
  Usually OpenVZ based
  Need KVM/XEN/VMWare to support Quagga/BIRD
LowEndTalk.com
  Message board, various small scale VM hosts
Google
  “vps bgp session”

## Slide 13: Anynode in Detroit
Listing on LowEndTalk
  Asked if they could support BGP.
  Yes on any VPS!!
$80/yr, 1 CPU, 512mb, 40gb HDD, 500gb BW

## Slide 14: Indian bargin!
LeapSwitch, based in Pune, India.
  New VPS host, saw an offer advertised
$120/yr, 1gb RAM, 20gb HDD, 500gb BW

## Slide 15: Growing
Up to 4 VMs
  London A (on existing KVM server)
  London B
  Detroit
  India
Spinning up VM taking about 10 minutes
  Add JSON entry into RethinkDB
  Install Debian
  Install Puppet (Collectd, BIND, Quagga, custom daemons etc)
  Done

## Slide 16: Friends
Offers to host VMs for free from:
  Edinburgh @ Fluency
  Boston @ TorwardEx
One swap:
  Bremen, Germany @ Fremaks
Quickly up to 7 nodes after 1 month

## Slide 17: Friends
“We can host something, but not a VM”
Various issues:
  Network engineers didn’t have access to VM hosts
  No VM infrastructure at all
  All VMs routed by hypervisor, can’t bridge to BGP routers
Solution…
  Raspberry PI, $35
  512mb / 16gb SD Card
  800mhz (overclocked)

## Slide 18: Raspberry Pi
Sent RPI to Belfast – David Farrell @ Tibus
Ran NSD3 great, ~200qps
Adding / removing zones with NSD3 required service restart 
Swapped to PowerDNS, testing went ok
pdns_control segfault’ing on ARM
Gave in and moved to BIND

## Slide 19: Time to peer
Offer of a node at SFMIX from Matt Peterson
San Francisco based IXP
Couldn’t turn this down.
Zero U install
Needed 2 NICs, IX + OOB
  FitPC2i - perfect 
  Atom 1.6ghz, 1gb RAM, 16gb SSD
  $150 on eBay
Peering with:
  HE.net, ISC, Unwired
  Layer42, Lookout

## Slide 20: Pi problems
Puppet slow + loading zones taking too long
More offers to host h/w nodes
  Manchester, Andy Davidson @ Allegro
Gigabyte BRIX
  1.8ghz, 4gb RAM, 30gb MSATA
Swap out Belfast Pi

## Slide 21: Still growing
11 live nodes
  London C, VPS from Thomas Greer @ TSONE
Bahrain on its way

## Slide 22: Fun along the way
First BGP customer for some of the LowEndTalk advertisers
  Assisted educating them…
  Prefer transit routes over customers, eek
Some hosts don’t have communities
  Helping people get those implemented
RIPE Atlas
  Scheduled measurements to look at latency + CHAOS id.server

## Slide 23: Market for VMs with BGP sessions

## Slide 24: Discoveries
Easy to find budget anycasters
  Webhost forums / LowEndTalk / bgp.he.net
“Interesting” deployment methods
  Shared /24
    Dedicated IP, custom fwd/rev DNS, slaved zones
  Hosted /24
    Same as above but customer provides /24 to announce
  Shared /24, /32 tunneled
    Dedicated IP, tunneled by anycaster to customer via GRE
  Single /24
    Anycaster only has one /24, website + mail + mgmt in same space. DNS answered at edge, other IPs tunneled to another VM/dedicated box.

## Slide 25: Discoveries
Not all budget DNS hosting companies host every zone at the edge
  Some host zones centrally and cache at the edge
Many tunnel all DNS traffic back to a single location
  Looks like anycast
  Poor DNS performance

## Slide 26: Not just DNS?
Simple HTTP/HTTPS service to assist debugging
  local.esgob.com
  local4.esgob.com / local6.esgob.com
Returns JSON via lighttpd on each node
nat@enw:~ $ curl http://local.esgob.com
{
"city": "London",
"country": "England",
"countryiso": "gb",
"flag": "england",
"locationdisplay": "England, London, B",
"ref": "ql7f823b"
}

## Slide 27: What next?
Keep honest – host every zone at the edge
Finish API + web interface
Open source more code
Support:
  Multi master
  TSIG inbound
Public SOA checker
Mix of routing and DNS daemons
  configurable per node in RethinkDB
  BIND, NSD4, KNOT, Quagga + BIRD

## Slide 28: What next?
Move to BGP sessions to full table
  Archive MRT dumps
  Maybe BIRD, don’t need full table in the kernel
Crypto loopback file system on remote nodes
Fix v6 routing – peer with HE in Europe
Find more friendly hosts:
  Eastern Europe
  Transit in west coast US
  Especially in Afria, Asia + South America
  Wales!
Currently costing just under $480/yr

## Slide 29: Questions?
https://noc.esgob.com
NAT-RIPE
@natmorris @esgobltd