## Slide 1: Increasing the Zone Signing Key Size for the Root Zone
Duane Wessels
DNS-OARC 24, Buenos Aires
April 1, 2016

## Slide 2: Presentation Outline
Current root zone DNSSEC parameters
Schedule
Change details
Consequences of a 2048-bit ZSK
Fallback plan

## Slide 3: Initialisms
KSK | Key Signing Key | Operated by IANA/ICANN
ZSK | Zone Signing Key | Operated by Verisign
KSR | Key Signing Request | XML-formatted bundle of keys to be signed
SKR | Signed Key Response | XML-formatted bundle of signatures

## Slide 4: This is not the KSK Rollover
You may have recently heard about work underway to roll the root zone Key Signing Key (aka Trust Anchor).
That’s not what this is.
Verisign is working closely with the other Root Zone Management partners to ensure that the ZSK length change does not coincide with other activity that would increase the root zone DNSKEY response size.

## Slide 5: Current DNSSEC parameters
Parameter | KSK | ZSK
Algorithm | 8 | 8
Size | 2048-bits | 1024-bits
Rolled | (not yet*) | quarterly
Re-sign period | 10 days | 12 hours
Signature validity | 15 days | 10 days
Signs | DNSKEYs | everything else
ZSK size will be increased to 2048-bits
No other parameters will be changed
*Sticklers will bring up the DURZ transition in 2010

## Slide 6: Schedule
Date | Milestone
2016-04-15 | Testing between ICANN and Verisign
2016-05-12 | KSK ceremony #25; sign 2016Q3 ZSKs
2016-08-11 | KSK ceremony #26; sign 2016Q4 ZSKs
2016-09-21 | First 2048-bit ZSK pre-published in root zone
2016-10-01 | Root zone signed with 2048-bit ZSK

## Slide 7: Schedule
Notes: This is a graphic representation of the schedule, showing KSK ceremonies and the publication of keys signed at each ceremony.

## Slide 8: Schedule
Notes: Highlighted area shows the first time a 2048-bit key is published in the root zone.
This key is signed at Root KSK Ceremony in Q2 (May).

## Slide 9: Rollover Details

## Slide 10: The ZSK Rollover Process
ZSK is Rolled quarterly
Quarter is divided into 9 slots of 10 days each
  Sometimes the 9th slot is longer
The DNSKEY RRSIG record changes in each slot
Uses pre-publish technique
  Incoming ZSKs pre-published for one slot (9th slot)
  Outgoing ZSKs post-published for one slot (1st slot)
Size of DNSKEY response message increased due to pre-/post-publish

## Slide 11
DNSKEY
response
size increase
DNSKEY
response
size increase
Notes: As background, first we describe the normal quarterly rollover process.
Point out on the diagram: quarters, slots, colored boxes represent DNSKEY RRSIGs, pre- and post-publish
Note size of DNSKEY response message increases on quarter boundaries due to pre-/post-publish, but only one key signs at a time so other responses do not increase in size.

## Slide 12
Old 1024-bit ZSK will be
post-published through slot 3.
Notes: Key points:
very much like normal 1024 rollover, except we introduce 2048-bit key (light green box)
the outgoing 1024-bit key will be post-published for longer than normal (3 slots instead of 1)
DNSKEY response size will be larger with 2048-bit keys. We’ll talk about that later.

## Slide 13: 1024-2048 Rollover
Much like normal 1024 rollover
Except longer post-publish period for outgoing 1024-bit key
  ...just in case
Notes: Say more about the longer post-publish and “just in case” when talking about fallback later in the presentation.

## Slide 14: Consequences of a 2048-bit ZSK

## Slide 15: Size of Signed DNSKEY Response
DNSKEY response size changes throughout this process
Normal (non-roll) size increases from 736 to 864 octets
ZSK rollover size increases from 883 to 1138 octets
Future KSK revoke size would be 1425 octets
Notes: The bars in this chart are ordered by time that these events would occur, starting at the top with a normal 1024 ZSK and ending at the bottom with a 2048-2048 rollover.

## Slide 16: Size of Other Signed Responses
All non-DNSKEY RRSets are signed by the ZSK
DO=1 responses will be larger
1024-bit ZSK signature (RRSIG) : 159 octets
2048-bit ZSK signature (RRSIG) : 287 octets
But its not that simple....
We replayed real query logs to various DNSSEC configurations to understand traffic impacts

## Slide 17: Measurement Methodology
Captured 10 minutes of queries sent to a.root-servers.net
Signed a root zone with various DNSSEC configurations
Replayed traffic over both UDP and TCP
  Including client EDNS0 UDP message sizes and DO flag values
Recorded the response size, TC flag, etc.

## Slide 18: Quick Stats
Zone File
  SOA Serial 2016022401
Input Trace:
  February 24, 2016
  22:00:00 -- 22:10:00 UTC (10 minutes duration)
  40,993,338 IP packets captured
  37,494,153 DNS UDP queries captured
    62,490 queries/second
  A-root sites: NYC3, LON3, LAX2, FRA1, HKG5

## Slide 19: Fragmentation
Essentially zero fragmentation. Only responses to “ANY” queries exceed the fragmentation limit. Very few of those in the input trace.

## Slide 20: Truncation -- DNSKEY
Notes: This shows how many DNSKEY responses would be returned with TC=1 in a UDP response.
The difference between “1024 normal” and “1024-1024 roll” is about 150 bytes, but it is enough to result in much more truncation.

## Slide 21: Truncation -- All
Notes: Taking all responses together (not just DNSKEY responses) the level of truncation really only depends on the size of the ZSK.
In the “1024-2048 pre pub” mode (red) we are still signing with the 1024-bit key.
whereas in the “1024-2048 post pub” mode (brown) we are now signing with the 2048-bit key.

## Slide 22: Response Size Distribution
The size of the key used for signing determines the difference in response sizes.
Lines with the same signing key size are stacked on top of each other.
Notes: Similar to previous slide, the size distribution only depends on the size of the ZSK.

## Slide 23: Bandwidth
This is the bandwidth measured by the simulation for a single root server letter (A).
Notes: This is mostly of interest to root server operators.
Their response bandwidth will increase noticeably due to the 2048-bit ZSK

## Slide 24: Fallback Plan

## Slide 25: Need for Fallback
We fully expect the length change to occur without incident
However, unforeseen problems may be beyond our control
Should it be necessary, we are prepared to revert to a “known good state”
  i.e. a 1024-bit ZSK
In fact the exact same 1024-bit key just prior to the length change

## Slide 26: Dual KSRs / SKRs
In support of this fallback plan, ICANN will sign two KSRs at two root KSK ceremonies:
The 2048-bit ZSK
  plus associated post-publish and pre-publish keys
The fallback 1024-bit ZSK
  plus associated post-publish and pre-publish keys

## Slide 27
Notes: This is much like a slide shown earlier, except now we also so the fallback KSR at the bottom

## Slide 28
Notes: Point out that we plan to reuse the Q3 key as the Q4 fallback key.

## Slide 29
Notes: The green boxes show the sets of keys that will be submitted for signing at the May ceremony

## Slide 30
Notes: And blue shows the key sets that will make up the two KSRs at the August ceremony

## Slide 31: Fallback Criteria
Something unforeseen
Something very serious
Something that can not be solved by (temporarily) disabling DNSSEC validation

## Slide 32: Important Milestones
Introduction of 2048-bit ZSK to zone (pre-publish)
  Slot 9 of Q3
Zone signed by 2048-bit ZSK
  Slot 1 of Q4
  Cached RRSIGs will expire over the course of a few days
Removal of old 1024-bit ZSK (end of post-publish)
  Point of No Return

## Slide 33: A “Slot 9” Fallback
If a problem arises during the slot 9 2048-bit pre-publish phase:
Simply un-publish the 2048-bit ZSK from the root zone
Publish only the current 1024-bit ZSK
Continue signing with the current 1024-bit ZSK
There will be no ZSK roll for the next calendar quarter

## Slide 34: A “Slot 1” Fallback
If a problem arises during slot 1 after signing with the 2048-bit ZSK:
Revert to signing with the old 1024-bit ZSK
  It is still being published
When to remove 2048-bit ZSK from zone depends on nature and severity of problem

## Slide 35: Questions?