## Slide 1: Using Anycast to Balance Local Regulatory Demands with Global Availability
2025-OCT-08
Kate Gerry
Director of Interconnection
kate@netactuate.com
Notes: I am Kate Gerry, Director of Interconnection at NetActuate
We provide edge compute, used by multiple gTLD and ccTLD providers due to our extensive Anycast tuning.

## Slide 2: What is Anycast?
Announcement of the same /24 globally
  Anycast works best for UDP services, but many networks are using Anycast for TCP
  Easy to deploy, can be difficult to maintain
The more diverse your Anycast POPs, the more granular your control
  This offers you the ability to perform rolling maintenance without an interruption in services
Notes: Simply put, Anycast is announcing the same BGP prefix across the internet, from geographically diverse nodes.
It takes a lot of tuning to prevent sinkholes, where traffic may originate in Brazil but a provider will choose a ‘cheaper’ peering path in Europe over local transit in Brazil.
  This commonly occurs because regional ISPs will peer on IX route-servers in far-off regions, but refuse to peer locally, causing scenic routing.
The more countries that you deploy in, the more granular your control.

## Slide 3: Common Anycast Problems
ISPs join and leave Internet Exchanges without notice
  Often networks leave IXes in local markets but stay connected to foreign exchanges
Performance issues are often discovered by customer complaints, since you cannot have eyeballs in every customer market
  Monitoring can be done by checking flow against GeoIP data, but you cannot troubleshoot every ASN, only the most popular
Notes: ISPs still end up increasing their local-preference for those IX routes, causing scenic routing across oceans instead of utilizing local transit
  Some large transit networks do not accept BGP communities to force transit routes to have the same local preference as peering
    This same network will provide IPv6 transit over peering, with the same increased local preference
    This has caused a lot of issues and confusion when an IPv6 peering session is turned up as transit by accident
Customers sometimes attempt to augment their anycast deployment themselves, without notifying your NOC first. For example, I had a customer sinkhole all of their traffic to a random provider in New Zealand, effectively causing a partial outage.
  When this happens, what does the customer do? They complain at you of course!
    This is where having a NOC that can quickly identify the source of the problem quickly is a requirement
  Thankfully this is easily solvable with a quick "BGP Shut"

## Slide 4: Recent Problems
Increased government regulations
  Enforcing localized logging and reporting requirements
  Content blocking
  Data sovereignty
Legal orders
  Block specific domains in individual regions
  Direct traffic to a government "black box"
High latency and Load balancing
  Sites/services have a lot more international users
Notes: Government regulations include logging and reporting.
Censorship is no longer limited to authoritarian regimes, now court orders are forcing content providers to restrict content depending on geographic region.
If you want to continue doing business in those countries, you must abide by those orders.

## Slide 5: Solutions
Do nothing, do not utilize Anycast
  Possibility of legal ramifications, DNS and/or IP blocking
  Performance depends on how geographically close the user is to the server
Comply with the legal order globally with or without Anycast
  This approach reduces your legal liability
  Impacts customers the most
  The laws of the United States impact the users of Ireland
Notes: This has been the solution for common
The easiest way to handle this is to follow your local countries laws and tell the rest of the world "No"
Doing this can cause you a world of hurt, with overly broad court orders possibly blocking your traffic
Even when complying with all laws, you still "pick and choose". For example, 'Your pornography website is illegal in our country, comply with our regulations "or else"' letters throughout the years

## Slide 6: Solutions (Cont)
Ingest a GeoIP database
  Deal with false-positive / false-negatives
  Increased development cost
  This can be done hand-in-hand with Anycast
Comply with legal orders in-region with Anycast
  Easily block xyzstreamingsports.io where a legal order is enforced by applying the changes on a single region
  As a side effect, globally, users will have low latency responses, improving performance
Notes: GeoIP: You can comply with legal requirements by investing in your development team and increase complexity by adding a GeoIP module.
This can increase CPU usage and you're reliant on the accuracy of the database, not where the packet originated from.
Anycast: You can censor or create custom A/Quad A records for specific domains on a per-locale basis.
You could also do Anycast with TCP and have your entire site in that region custom for local regulations.
Anycast for DNS and GeoIP databases requires multiple records depending on the legal situation
Anycast for TCP will require mirrored databases/etc
In all cases, Anycast will require a globally mirrored deployment

## Slide 7: Solutions (Cont)
Comply with a government's "pen register" orders
  Only give them PCAP data from the regions that they have authority in
Direct users to local edge compute clusters
  This delivers the application to the user locally, with minimal crossing of international borders
  Works hand-in-hand with Anycast
Notes: One point of pain are pen register orders. If you're lucky, they will accept your logs, but if you're unlucky, you will have a court order to connect their monitoring device(s) to your hardware, sniffing all traffic.
  They are just looking at Source/Destination headers, so SSL doesn't really matter.
Only enable exhaustive logging on clusters where the local laws demand it. This way you can limit the amount of storage your logs require, maintain more customer privacy.
There is uncertainty whether Anycast works well for TCP applications, which in most cases it works just fine, like any other ECMP load-balanced application, you're just going across the internet. If you're afraid of deploying like this, it may make sense to direct users to unicast address space for local compute.
One of the benefits of deploying your compute with Anycast is that your DNS resolver is remote from your end-user.
  When the destination IP address is anycast, the end-user will always direct to the logically closest compute node.

## Slide 8: Thank you
2025-OCT-08
Notes: Thank you for putting up with me today! This is my first presentation, so I apologize for all rough edges!