## Slide 1: Anycast DNS Local Nodes and Routing Problems due to Asymmetric Routing on Internet Exchanges
Klaus Darilion · Head of Operations · klaus.darilion@nic.at
DNS OARC 45, 7.+8.10.2025 Stockholm

## Slide 2: Executive Summary
BCP 38 / RFC 2827: Network Ingress Filtering
  Prevent IP address spoofing
Anycast DNS Local Node
  Anycast Prefix only announced to IX
Asymmetric Routing
  Request received via IX
  No route to send response on IX
 If that 3 meet together -> Problem

## Slide 3: 1. BCP 38
ISP assigns one or more IP address to a customer
ISP verifies src IP of packets sent by the customer
  must be one of the assigned addresses
  then ISP will route the packet
customer uses a wrong source IP address
  packets are dropped
Internet
ISP 176.58.88.0/21
Customer-IP 176.58.91.106
src= 176.58.91.106
src=8.8.8.8
X
Many of our providers perform BCP38 filtering

## Slide 4: 2. „Local Node“
Let‘s describe terminology

## Slide 5: "Transit"
To talk with the "whole" Internet, we need a provider that forwards (transit) our packets to the destintations
This provider is called "transit provider" (or "upstream provider")
We have to pay the transit provider
Internet
Transit Provider e.g. Netactuate
RcodeZero

## Slide 6: "Peering"
Connectivity to some other networks (only that networks)
No connectivity to the remaining Internet
Usually free of costs (except switch port costs at the IX)
RcodeZero
Peers e.g. LINX, SwissIX, GigaPIX

## Slide 7: Anycast DNS Server Addressing
RcodeZero
Every server has 2 categories of IP addresses
  A Unicast (globally unique) IP address for the server management
  The Anycast IP addresses for the DNS service
My Notebook
Hidden Master DNS
Monitoring System
Statistics
SSH
AXFR
DNS Clients
DNS Clients
…
Anycast IP
Unicast IP

## Slide 8: RcodeZero „Global Node“
Single network link for:
  Management traffic
  Anycast DNS traffic
Transit for mgmt-traffic and anycast traffic
  The provider knows our mgmt IP
  The provider learns our anycast IP addresses (BGP)
  Allows outgoing data with mgmt and anycast IP as source
Internet, Peers and Tier 1
Transit Provider e.g. Netactuate
RcodeZero
BGP Anycast Prefix: src=194.0.25.0/24
Unicast IP
src=176.58.91.106

## Slide 9: RcodeZero Local Node (IX nodes)
The IX provides free colocation and IP connectivity for the server management
Additionally the DNS server is directly connected to an Internet Exchange (peerings)
The server has 2 network links
  Management traffic with transit
  Service traffic (Anycast DNS) with peerings only

## Slide 10: Anycast Local Node
The transit provider on the management link only knows the unicast IP address
  BCP38? On the manamgent link only traffic originating from that mgmt IP is accepted
Internet
Host e.g. TREX
RcodeZero
Peers
Unicast IP
src=195.140.195.86
BGP Anycast Prefix: src=194.0.25.0/24

## Slide 11: 3. Symmetric vs Asymmetric Routing

## Slide 12: Peering
RcodeZero Tampere
Every AS announces its own (and customer) prefixes to peers
194.0.25.0/24
195.74.0.0/19
Elisa AS719

## Slide 13: Symmetric Routing
Peer sends DNS request to us via IX
We respond with DNS Response via IX
DNS Response src: 194.0.25.10
dst: 195.74.4.6
RcodeZero
Elisa AS719
DNS Request src: 195.74.4.6
dst: 194.0.25.10
194.0.25.0/24
195.74.0.0/19

## Slide 14: Asymmetric Routing
Peer sends DNS request to us via IX
No Route to send Response via Internet Exchange
How to route the response?
RcodeZero
Elisa AS719
DNS Request src: 80.88.96.253
dst: 194.0.25.10
194.0.25.0/24
195.74.0.0/19
Internet
Host e.g. TREX
DNS Response src: 194.0.25.10
dst: 80.88.96.253
X
BCP38
Clients will experience timeouts!
(That‘s how we get aware of this issue.)
Unicast IP

## Slide 15: How to solve the issue?
We must forward the response to someone that routes it
Mgmt traffic provider should tweak BCP38 filter
  disable BCP38, static allow-list for our Anycast prefixes, ..
  preferred
  not always possible or simple not wanted
Beg for or buy transit from some ISP
  potential extra costs for transit or cross connect patches
  def. route via IX may break IX term
  takes time
Tunnel traffic to a global node
Or a combination of 2+3

## Slide 16
RcodeZero Local Node
Elisa AS719
DNS Request src: 80.88.96.253
dst: 194.0.25.10
Internet
Host e.g. TREX
DNS Response src: 194.0.25.10
dst: 80.88.96.253
Transit Provider e.g. Netactuate
RcodeZero Global Node
GRE Tunnel
DNS Response src: 194.0.25.10
dst: 80.88.96.253

## Slide 17: Implementation Routing
2 separate routing tables (idea from Aleksi Suhonen)
  default routing table for mgmt traffic
  table "2" for anycast DNS traffic
Feed IX routes into table 2
  route-map from-ix permit 10
  set table 2
Activate table 2 for Anycast DNS traffic
  routing-policy:
  - from: 194.0.25.0/24
  table: 2

## Slide 18: Implementation GRE Tunnel
Create GRE Tunnel
  tunnels:
  ip6gre-toglobal:
  mode: ip6gre
  local: 2a00:11c0:4a:10::165
  remote: 2a02:850:ffe7::1
Add default route into tunnel
  ! Make a static rule with higher distance !(eBGP=20, iBGP=200) to act only as fallback ! May be overruled by a BGP default route
  ip route 0.0.0.0/0 ip6gre-toglobal 250 table 2
  ipv6 route ::/0 ip6gre-toglobal 250 table 2

## Slide 19: Implementation GRE Tunnel
Create GRE Tunnel
  tunnels:
  ip6gre-toglobal:
  mode: ip6gre
  local: 2a00:11c0:4a:10::165
  remote: 2a02:850:ffe7::1
Add default route into tunnel
  ! Make a static rule with higher distance !(eBGP=20, iBGP=200) to act only as fallback ! May be overruled by a BGP default route
  ip route 0.0.0.0/0 ip6gre-toglobal 250 table 2
  ipv6 route ::/0 ip6gre-toglobal 250 table 2
Which global node
should be used?

## Slide 20: Anycast GRE
Automatic nearest node
Failover during global node maintenance
RcodeZero Local Node Tampere
RcodeZero Global Node Warsaw
RcodeZero Global Node Stockholm
RcodeZero Global Node Riga
2a02:850:ffe7::1 2a02:850:ffe7::1 2a02:850:ffe7::1

## Slide 21: Summary
Anycast GRE tunnel from local nodes to global nodes
Local host does BCP38?
  Default route for anycast DNS traffic into GRE tunnel
  Optionally add BGP-based default route sponsored by a local ISP (can be added later)
We still support IXs with local nodes
How do others anycast providers with local nodes solve the problem?

## Slide 22
Klaus Darilion · Head of Operations
klaus.darilion@nic.at