## Slide 1
LLMs for DNS Abuse Detection:
Promising or Overhyped?
(early-stage work)
Jihye Kim
Network Security Researcher
DNS-OARC 45

## Slide 2
LLMs are Everywhere!

## Slide 3
LLMs are Everywhere!

## Slide 5
LLM-Assisted PRotocol Attack Discovery
[1] Aygun, R. Can, Yehuda Afek, Anat Bremler-Barr, and Leonard Kleinrock.
“LAPRAD: LLM-Assisted Protocol Attack Discovery,” IFIP Networking IOCRCI Workshop

## Slide 6
LLMs for DGA Detection
[2] Alqahtani, Hamed, and Gulshan Kumar. “Large Language Models for Effective Detection of Algorithmically Generated Domains: A Comprehensive Review.” Computer Modeling in Engineering & Sciences 144, no. 2 (2025): 1439.

## Slide 8
Symbolic and text-based: naturally fits LLM tokenization
Human-readable, structurally complex
Real-world attack surface with diverse threats
Benchmark for structured reasoning
DNS for LLMs: Why DNS is a good input?

## Slide 9
DNS for LLMs: Why DNS is a good input?
Symbolic and text-based: naturally fits LLM tokenization
Human-readable, structurally complex
Real-world attack surface with diverse threats
Benchmark for structured reasoning

## Slide 10
DNS for LLMs: Why DNS is a good input?
Symbolic and text-based: naturally fits LLM tokenization
Human-readable, structurally complex
Real-world attack surface with diverse threats
Benchmark for structured reasoning

## Slide 11
DNS for LLMs: Why DNS is a good input?
Symbolic and text-based: naturally fits LLM tokenization
Human-readable, structurally complex
Real-world attack surface with diverse threats
Benchmark for structured reasoning

## Slide 12
Semantic / context detection
Prompt-based Zero / Few-shot generalization
Explainability via natural language
Actionable response generation
LLMs for DNS: Why LLMs are good for DNS?

## Slide 13
Semantic / context detection
Prompt-based Zero / Few-shot generalization
Explainability via natural language
Actionable response generation
LLMs for DNS: Why LLMs are good for DNS?

## Slide 14
Semantic / context detection
Prompt-based Zero / Few-shot generalization
Explainability via natural language
Actionable response generation
LLMs for DNS: Why LLMs are good for DNS?

## Slide 15
Semantic / context detection
Prompt-based Zero / Few-shot generalization
Explainability via natural language
Actionable response generation
LLMs for DNS: Why LLMs are good for DNS?

## Slide 16
Aspect | Traditional ML/Statistical Approach | LLM-based Approach
Input
Adaptability
Explainability
Attack
Coverage
Weakness
Hand-crafted features,
flow statsistics
Strong in-domain;
Weaker on novel attacks
Limited
(scores, feature weights)
Good for volumetric
& known patterns
Efficient but brittle
to unseen variants
Raw/semi-structured DNS sequences + features
Prompt-based zero/few-shot;
adapts with minimal training
Natural-language explanations,
Human-readable reasoning
Broader: flooding, amplification, semantic abuses, policy misuses
Higher cost/latency,
adversarial risks
LLMs vs. Traditional Methods

## Slide 17
Create Synthetic DNS Attack Traffic
Detect and Explain DNS Attack Traffic
Confuse Detector with Adversarial Traffic
LLMs for DNS: How Can LLMs be effectively used?

## Slide 18
Create Synthetic DNS Attack Traffic
Detect and Explain DNS Attack Traffic
Confuse Detector with Adversarial Traffic
LLMs for DNS: How Can LLMs be effectively used?

## Slide 19
DNS Abuse Taxonomy
DNS as tool or target for DDoS
Victim
Attacker
Resolver
Authoritative server
Flooding
Reflection / Amplification
Redirection
Subversion
DNSSEC Abuse

## Slide 20
DNS Abuse Taxonomy
Flooding
Reflection
/Amplification
Redirection
Subversion
DNSSEC Abuse
Abuse Type Description Related DDoS Vector
Sending excessive DNS queries
to exhaust server resources
Exploiting resolvers to reflect
and amplify traffic toward a victim
Manipulating DNS responses to
redirect traffic (e.g., to a botnet controller)
Compromising domain registration
or zone control to manipulate traffic
Abusing DNSSEC’s large responses or misconfigurations to overwhelm systems
Direct DDoS,
Resource exhaustion
Amplification DDoS
Indirect DDoS,
Traffic Manipulation
Indirect DDoS,
Traffic Manipulation
Amplification DDoS,
Resource exhaustion

## Slide 21
DNS Abuse Taxonomy
Abuse Type Description Related DDoS Vector
DNSSEC Abuse | 
Flooding
Reflection
/Amplification
Redirection
DNS
Subversion
Response Flooding
NXDOMAIN Flooding
(slow drip, random subdomain)
iDNS
TsuNAME
Unchained
NXNS Attack
NRDelegation Attack
Loop Attack
Query Flooding
Kaminsky Attack
DNS Cache Poisoning
SAD DNS
Domain Hijacking
Packet Interception
DNS Tunneling
Fast Flux
DGA (Malware C2 Infra)
DNSSEC Amplification
NSEC/NSEC3 Walking
Bogus DNSSEC Data Injection
Algorithm Downgrade Attack
Class
Subclass
Class
Subclass
Resolution Failure Flooding
(domain lock-up,
phantom subdomain)

## Slide 22
DNS Abuse Taxonomy
Abuse Type Description Related DDoS Vector
DNSSEC Abuse | 
Flooding
Reflection
/Amplification
Redirection
DNS
Subversion
Response Flooding
NXDOMAIN Flooding
(slow drip, random subdomain)
iDNS
TsuNAME
Unchained
NXNS Attack
NRDelegation Attack
Loop Attack
Query Flooding
Kaminsky Attack
DNS Cache Poisoning
SAD DNS
Domain Hijacking
Packet Interception
DNS Tunneling
Fast Flux
DGA (Malware C2 Infra)
DNSSEC Amplification
NSEC/NSEC3 Walking
Bogus DNSSEC Data Injection
Algorithm Downgrade Attack
Class
Subclass
Class
Subclass
Resolution Failure Flooding
(domain lock-up,
phantom subdomain)

## Slide 23
DNS Abuse Taxonomy
Attack Name Key Characteristics Traffic Features
Traffic
Generation
LLM
Detectability
Deception
Risk
NXDOMAIN
Flooding
Random/non-existent
Subdomains
RCODE(3)_ratio ↑
query_rate_and_entropy ↑
unique_qname_count ↑
qname_dist_entropy_norm ↑
Easy
High
Moderate

## Slide 24
dns_attack_taxonomy.json
- Class / SubClass
- Explanation
- Feature_Conditions
- Example_Instance
RAW (.pcap)
dns_extractor.py
compute_features.py
llm_formatter.py
FLAN-T5
Model
dns_llm_train.json
dns_llm_val.json
> input_text: prompt
> target_text:
structured JSON
From
data
collection
…
Knowledge Base
(Protocol + Attack knowledge)
Gradio Web UI
app_dns_t5.py
train_t5.py
predict_t5.py
cluster.py
DNS Abuse Detection WorkFlow

## Slide 25
Input
Model
Output
Which datasets/features?
Which LLM family/version?
How you’ll feed data?
What you want back?
DNS Abuse Detection WorkFlow

## Slide 26
Input
Input Models
- Benign traffic:
> OPENINTEL datasets (ground baseline)
- Attack traffic:
> Open-source attack datasets
- Traffic Generators + LLM-augmentation
> Flamethrower
> Scapy, TRex, MoonGen
(Optional)
Q. Traffic logs from DNS Operators?
Which datasets/features?
Public
Datasets
Synthetic
Attack Datasets
Adversarial
Traffic
Datasets
DNS Server
Logs

## Slide 27
Input
Input Models
Which datasets/features?
Public
Datasets
Adversarial
Traffic
Datasets
DNS Server
Logs
- Traffic Generators + LLM-augmentation
> Flamethrower
> Scapy, TRex, MoonGen
- Benign traffic:
> OPENINTEL datasets (ground baseline)
- Attack traffic:
> Open-source attack datasets
Synthetic
Attack Datasets
(Optional)
Q. Traffic logs from DNS Operators?

## Slide 28
Input
Input Models
Which datasets/features?
RAW (.pcap)
dns_extractor.py
llm_formatter.py
compute_features.py
STD_COLS (Local Features)
frame.time_epoch, ip.src, ipv6.src,
dns.flags.response, dns.qry.name, dns.resp.name,
dns.resp.ttl, dns.resp.len, dns.flags.rcode,
dns.count.answers, dns.count.add_rr,
udp.length, frame.len

## Slide 29
Input
Input Models
Outputs for DNS analysis
and LLM prompting:
--mode packet
Fine-grained per-packet context
+ file-level aggregates
--mode window
Sliding-window aggregaton over
--window seconds;
> Per-window features
Which datasets/features?
RAW (.pcap)
dns_extractor.py
llm_formatter.py
compute_features.py

## Slide 30
Input
Input Models
Which datasets/features?
RAW (.pcap)
dns_extractor.py
llm_formatter.py
compute_features.py
Converts ‘features.csv’ into JSONL
for T5 training or inference prompts
--mode infer
Build/keep ‘input_text,’
append schema suffix, and write
all prompts to ‘out_val’
--mode train
Requires ‘label’;
performs safe train/val split
Use taxonomy to build ‘target_text’

## Slide 31
LLM Models
Type | Models | Key Characteristics
Decoder-only |  | 
Encoder-only |  | 
Encoder-Decoder |  | 
We need “ Classification + Explanation + Generation + … ”
Model
Strong at log/query generation
Autoregressive: predicts next token sequentially
Less suitable for classification/detection tasks
GPT-Family,
LLaMA
BERT-,
Family
T5,
BART,
UL2
High accuracy in detection/classification
Cannot generate outputs;
Limited explanatory power
Supports detection, explanation, and generation
Larger parameter size / higher computational cost
Which LLM family/version?
How you’ll feed data?

## Slide 32
LLM Models
T5: Text-to-Text Transfer Transformer
Model
Which LLM family/version?
How you’ll feed data?

## Slide 33
LLM Models
Model
T5 Training & Inference Scripts
train_t5.py
Fine-tunes T5 on DNS prompts/targets with robust metrics
Tokenizer/Model: AutoTokenizer, AutoModelForSeq2SeqLM
predict_t5.py
Batch-generated normalized single-line JSON per input
FLAN-T5
Model
train_t5.py
predict_t5.py
app_dns_t5.py
Which LLM family/version?
How you’ll feed data?

## Slide 34
LLM Models
Model
Which LLM family/version?
How you’ll feed data?
Self-attention
Cross-attention
12x
Encoder
12x
Decoder
Formmated DNS Log
JSON token
sequence
T5-Base Model
large
small
…

## Slide 35
LLM Models
- Knowledge base as RAG:
> Up-to-date data reasoning from RFCs
and attack reports
Model
Which LLM family/version?
How you’ll feed data?
Flan-T5
Knowledge Base
search
retrieve
- DNS attack taxonomy for LLM Inference:
dns_attack_
taxonomy.json
kb_rfcs.json
kb_attacks.json

## Slide 36
Output Models
What you want back?
PCAP to Inference: End-to-End Demo
- Gradio Web UI
Summary Card (Gradio HTML):
- Class
- Subclass
- Score
- Explanation
- Mitigation
CSV (labelled):
per-row + final aggregated label
FLAN-T5
Model
train_t5.py
predict_t5.py
app_dns_t5.py
Output

## Slide 37
Output Models
What you want back?
PCAP to Inference: End-to-End Demo
- Grafana/Prometheus
Prometheus:
- exports/metrics (port: 9108);
Grafana Panels:
- dns_pipeline_seconds
- dns_label_ratio
- dns_final_score
- dns_nxdomain_ratio …
FLAN-T5
Model
train_t5.py
predict_t5.py
app_dns_t5.py
Output

## Slide 38
Future Work
Short-term: Datasets, Benchmarking
> Benchmark diverse DNS datasets
> Compare across model families (Traditional MLs vs. LLMs)
Mid-term: Develop a Synthetic / Adversarial Traffic Framework
> Adversarial Robustness Testing
> Improve Trustworthiness
Long-term: Towards Operator-grade Deployment

## Slide 39
Simple DEMO (3m)