## Slide 1: Trust your paths Routing security for DNS infrastructure operators Ritesh Mukherjee
OARC 47 Vancouver
RPKI / ROV
ASPA
BMP
Anycast dns

## Slide 2
You instrument everything above the routing layer
YOUR DASHBOARDS WATCH
Query rate and QPS per instance
Response latency percentiles
RCODE mix — NOERROR, SERVFAIL, NXDOMAIN
DNSSEC validation failures
Zone serial propagation
THEY DON'T SEE
Who is originating your prefix right now
Whether a more specific one exists somewhere
Which AS path traffic takes to reach you
Why a query landed on the instance it did
Whether the "instance" is yours at all
When routing breaks, DNS signals often stay healthy — right up until they don't.

## Slide 3
Three incidents, three different failures
Each needed a different mechanism to catch it
2018
Amazon Route 53
More-specific hijack of an authoritative DNS service. Resolvers worldwide cached forged answers.
2023 – 2025
Root server prefixes
Repeated origin hijacks — mostly invisible because anycast localizes the damage.
2024
Cloudflare 1.1.1.1
An origin hijack and a separate route leak in the same hour. ROV catches one of them.

## Slide 4
April 24, 2018
11:05 UTC
eNet (AS10297), an ISP in Columbus, Ohio, starts announcing
five /24s carved out of Route 53's authoritative DNS space.
Incident 1 — Amazon Route 53

## Slide 5: The Cascade
AS10297 announces 205.251.192.0/24, .193, .195, .197, .199
Peers prefer the more-specifics over Amazon's /23
Resolvers querying Route 53 reach an impostor authoritative
It answers for one name only: myetherwallet.com
Users land on a phishing clone with a self-signed certificate
The Impact
    bogus routes present, 11:05 – 13:03 UTC
    Route 53 IP addresses covered by the hijacked /24s
    in Ether drained from the wallets of users who clicked through the certificate warning
    AWS systems compromised — the attack lived entirely in routing
~2 hrs
~1,300
~$150K
0

## Slide 6
You didn't have to accept the route to be hit
Large public resolvers—including 1.1.1.1—sat behind routers that accepted the bogus /24s. They queried the impostor and cached its answers for everyone behind them.
Caches outlive the hijack
Withdrawing the route doesn't flush a resolver. A forged answer keeps being served until its TTL runs out.
ROV would have caught it
A ROA for the /23 with maxLength /23 makes every one of those /24s — from any origin — RPKI-Invalid.
DNSSEC limits the damage
A signed zone and a validating resolver turn a forged answer into SERVFAIL. Integrity holds; reachability doesn't.

## Slide 7
A recurring target
    F-root IPv6 originated by AS24028. Seen by a single RIS peer — the prefix had a ROA
    Jan 2023
    E-root and F-root IPv6 originated by AS17639 for 18+ hours. E-root had no ROA — its blast radius was about 3× larger than F-root's.
    Feb 2023
    L-root IPv4 originated by AS137661, prepended seven times. Best-path selection hid it from almost every collector.
    Apr 2023
    K-root IPv4 announced from a hosting partner's own AS instead of AS25152. Visible only in Italy.
    Jun 2023
    Eight root prefixes, including A-root, originated with AS35168 — the first documented BGP hijack of root server prefixes.
    Jun 2025
    L-root IPv4 originated by AS3132. Only 19 BGP monitors saw it, yet ~10% of ThousandEyes agents sent L-root queries through it.
    Jun 2025
Incident 2 — Root server prefixes
Sources: ThousandEyes / Code BGP root-prefix monitoring; RSO statement on the June 2025 hijack.

## Slide 8
Eight root identifiers, one bogus origin
JUNE 20, 2025
AS35168
TNS-Plus, Kazakhstan
AS28910
Uzbektelekom — no ROV
Regional resolvers
query unauthorized "roots”
Further spread stopped by policy, topology, best-path —not by validation.
19:40 routes appear · 19:42 alert · 21:10 withdrawn
bogus origin
A-root
198.41.0.0/24
B-root
170.247.170.0/24
C-root
192.33.4.0/24
F-root
192.5.5.0/24
G-root
198.41.0.0/24
H-root
170.247.170.0/24
J-root
192.33.4.0/24
M-root
202.12.27.0/24
Three of these prefixes had covering ROAs. It didn't matter: the one network that accepted the routes doesn't do Route Origin Validation. Verisign's own tooling raised the alarm within two minutes.

## Slide 9
Anycast is camouflage
The property that makes anycast resilient is the same one that hides a hijack from you.
ROAs measurably shrink the blast radius. Same hijacker, same day: the unsigned E-root prefix spread about three times farther than the signed F-root prefix.
Best-path hides it
A router only propagates its best path. A bogus route that loses locally never reaches the collectors — L-root in 2023.
Seeing it takes your own vantage
Verisign caught 2025 in two minutes with its own tooling. Your edge routers already receive what your peers send — if you look.
The damage is local
Only the catchment behind the bad route is affected. Global health checks from your usual vantage points stay green.

## Slide 10
1.1.1.1
An origin hijack and a route leak of the same resolver, starting within one minute of each other.
Unreachable or degraded from 300+ networks in 70 countries
Incident 3 — June 27, 2024

## Slide 11
1.1.1.1 — what happened, minute by minute
    AS267613 (Eletronet) starts originating 1.1.1.1/32 to peers, providers, and customers.
    18:51
    AS262504 (Nova) leaks 1.1.1.0/24 to its upstream AS1031. Path: 1031 262504 267613 13335.
    18:52
    AS1031 redistributes the leak to IX peers and route servers. A Tier 1 takes the /32 as a blackhole route.
    18:52
    Cloudflare raises an internal incident — 72 minutes after onset.
    20:03
    The leak reappears via 262504 53072 7738 13335. Queries now succeed — with high latency.
    20:10
    Blackholing appears to be resolved after Cloudflare shuts down two peering points with AS267613. The leak continues to pull traffic to São Paulo.
    22:16
All times UTC. Source: Cloudflare incident report, July 4, 2024.
    AS262504 fully withdraws the leak — 7.5 hours after it began.
    02:28 +1

## Slide 12
Two failures, two different verdicts
Cloudflare's ROA: 1.1.1.0/24 → AS13335, maxLength /24
The leak was RPKI-valid. Every router doing ROV accepted it.
THE LEAK
1.1.1.0/24
path 1031 262504 267613 13335
Right prefix, right origin. The problem is the path: a customer re-announced a peer's route to its own provider.
ROV: Valid
THE HIJACK
1.1.1.1/32
origin AS267613
Wrong origin and longer than maxLength. A /32 also breaks the usual "nothing longer than /24 in the DFZ" filter.
ROV: Invalid

## Slide 13
What users — and DNS monitoring — saw
Neither symptom says "routing." A latency spike with NOERROR responses is the kind of alert that gets acknowledged and closed.
SYMPTOM 2
Correct answers, slowly
Traffic from the US and Germany landed in Brazilian data centers. Responses were right; the round trip wasn't.
THE TELL
BMP saw it arrive
Cloudflare's own pre-policy BMP data showed the /32 coming in from route servers — and their import policy rejected it.
SYMPTOM 1
Timeouts
Queries dropped inside AS267613 or at Tier 1, which blackholed the /32. Looks like packet loss.

## Slide 14
ROV: Is this origin allowed to announce this prefix?
MECHANISM 1
1.1.1.1/32 from AS267613
✗ Invalid
1.1.1.0/24 via leak
✓ Valid
right origin, wrong path — ROV can't tell
CATCHES
Origin hijacks and unauthorized more-specifics — Route 53 2018, every root-prefix event, the 1.1.1.1/32.
MISSES
Anything with the right origin and the wrong path: route leaks, forged-origin hijacks.
ONLY WORKS IF
You sign, and the networks between you and your users drop invalid. Uzbektelekom in 2025 and the Tier 1 in 2024 didn't.
No covering ROA → NotFound → accepted by default
ROA in RPKI
1.1.1.0/24 · AS13335 · max /24

## Slide 15
ASPA: Does this path match real provider relationships?
Each AS signs one statement: “These are my upstream providers." A path must climb from customer → provider, cross at most one peering, then descend.
MECHANISM 2
WALKING THE 1.1.1.0/24 LEAK FROM THE ORIGIN
AS13335 → ✗ → AS267613 → ✗ → AS262504 → ✓ → AS1031 → their peers
13335 → 267613 A peer, not a provider. Cloudflare's ASPA wouldn't list it.
267613 → 262504 Nova is Eletronet's customer. Eletronet's ASPA wouldn't list it.
262504 → 1031 A real provider. This hop is fine — the damage was done earlier.
Either ASPA on its own makes the path Invalid for anyone who receives it from AS1031 and validates it. Signing is in production at RIPE NCC, ARIN, and APNIC; LACNIC is due by the end of 2026. Roughly 1% of ASes have signed.

## Slide 16
Which mechanism catches which incident
INCIDENT | ROV | ASPA | DNSSEC
Route 53 more-specifics, 2018 | ✓ | — | ◐
Root prefix origin hijacks, 2023 – 2025 | ✓ | — | ◐
1.1.1.1/32 hijack, 2024 | ✓ | — | ✗
1.1.1.0/24 route leak, 2024 | ✗ | ✓ | ✗
✓ catches it, given signed objects and validating receivers · ◐ protects the answers, not the reachability · — not what it's for
DNSSEC protects your answers. ROV protects your origin. ASPA protects your path.

## Slide 17
One Scenario, live
Twenty minutes doesn't fit all three incidents, so we'll replay the one ROV can't see.
Live DEMO
20:10 UTC, JUNE 27, 2024
262504 53072 7738 13335
The leaked path successfully delivered queries to 1.1.1.1—from São Paulo, with high latency.

## Slide 18
The lab: an anycast resolver with two sites
Containerlab · FRR · Routinator validating against the live RPKI · RAVEN
AS13335 site GRU
1.1.1.0/24 · nsid "gru"
AS7738
AS53072
AS262504
leaker
AS1031
RAVEN
BMP in · RTR from Routinator
Vantage edge
eyeball network
DNS probe
dig +nsid @1.1.1.1, every 1s
Transit
normal path
AS13335 site YVR
1.1.1.0/24 · nsid "yvr"
leaked path, with added delay on the long haul
BMP

## Slide 19
Two panes, one event
Watch what each one says when the leak arrives
● ● ● pane 1 — DNS probe
What DNS monitoring sees.
Before: NOERROR, low latency, nsid=yvr
After: NOERROR, latency jumps, nsid=gru
● ● ● pane 2 — raven watch
What routing validation sees.
1.1.1.0/24 via AS1031
ROV: Valid ASPA: Invalid
posture: path-suspect
Every answer is correct. Nothing here says "routing" — it reads as a slow site.
Same moment, with the reason: the origin is legitimate, the path isn't.

## Slide 20
What a DNS operator can do this quarter
Sign every anycast prefix
ROAs with maxLength equal to what you announce. If you use a unique origin AS per site (RFC 6382), every one of them needs a ROA.
Publish ASPA
One object per ASN listing its actual transit providers— including per-site ASNs. Keep it current when a transit provider changes.
Watch from your own edge
Stream pre-policy BMP from your anycast edge routers. Alert on new origins, new more-specifics, and paths that fail ASPA.
Ask your transits
Do they drop RPKI-Invalid routes? How do they filter blackhole requests? Their answer decides whether your ROAs matter.
And keep signing zones and validating. DNSSEC is the layer that still holds when routing doesn't.

## Slide 21
The demo ran on RAVEN
A single Go binary that takes BMP from your routers and RPKI from your validator and tells you which routes have a valid origin and a valid path.
Open Source
    pre-policy Adj-RIB-In from any vendor's router
BMP
    VRPs and ASPAs from Routinator or any RTR v2 cache
RTR
    CLI, live stream, Prometheus
Out
● ● ● quick start
raven serve --bmp-listen :11019 \
--rtr rpki1.example.com:8323
raven watch --posture path-suspect
github.com/nokia/bgp-routing-security-monitor
BSD-3-Clause · no external measurement infrastructure required

## Slide 22: Your DNS can be perfectly healthy and still be answering from the wrong place. - Questions? - Ritesh Mukherjee
OARC 47 Vancouver